## Slide 1: Character device driver
Giảng Viên: Lưu An Phú

## Slide 2: Agenda
Objective
Implement file operation
Driver basic functions
Practice

## Slide 3: Driver main functions
Service user space
Call service from kernel space
Working directly with hardware

## Slide 4: Character device
Cây phân cấp device
  Character device
  Block device
  Network device

## Slide 5: Device file
All device file place in /dev folder
Major number
Minor number
Create a device file
  By udev
  By mknod command
  By device driver

## Slide 6: Device operation
open
close
read
write
ioctl

## Slide 7: Implement file operation in driver
static int dev_open(struct inode *inodep, struct file *filep)
static int dev_close(struct inode *inodep, struct file *filep)
static ssize_t dev_read(struct file*filep, char __user *buf, size_t len, loff_t *offset)
static ssize_t dev_write(struct file*filep, const char __user *buf, size_t len, loff_t *offset)

## Slide 8: Swap memory buffer
unsigned long copy_from_user(void *to, const void __user *from, unsigned long n);
unsigned long copy_to_user(void __user *to, const void *from, unsigned long n);

## Slide 9: Register file operation with kernel

## Slide 10: Basic steps of character driver
Define file operation
Define other interface
Initialize private resource
Create device file
Register file operation and other interface

## Slide 11: Create device file
alloc_chrdev_region
class_create
device_create
cdev_init
cdev_add

## Slide 12: Destroy device file
cdev_del
device_destroy
class_destroy
unregister_chrdev_region

## Slide 13: Compare create and destroy a device
Create device file
alloc_chrdev_region
class_create
device_create
cdev_init
cdev_add
Destroy device file
unregister_chrdev_region
class_destroy
device_destroy
cdev_del

## Slide 14: Example code

## Slide 15: Practice
Viết 1 driver tạo ra device file có tên /dev/sample_led. Mỗi khi user ghi 1 vào device file thì led sáng, user ghi 0 vào thì led tắt. Nếu led đang sáng, đọc file sẽ trả về 1, led tắt đọc file sẽ trả về 0.

## Slide 16: Ioctl
Driver code
  static long dev_ioctl(struct file *filep, unsigned int cmd, unsigned long arg)
User space code
  #include <sys/ioctl.h>
  int ioctl(int fd, unsigned long request, ...);

## Slide 17: Example code

## Slide 18: Home work
Viết 1 cặp ioctl tương ứng giữa driver và application. User có thể truyền command xuống để thực hiện nhấp nháy đèn led.
Cắm led vào bảng nhựa thành hình số 8, trong hàm init của driver thực hiện confile gpio, sau đó tạo ra device file. Khi ghi 1 số bất kỳ có 1 chữ số thì hiển thị lại trên led của bảng nhựa.

## Slide 19: Advanced home work
Viết 1 cặp driver và application. Khi hệ thống boot lên sẽ chạy application và insmod driver. Application sẽ tiến hành mount device file vào foldel /home/root/char_dev. Folder trên nếu không tồn tại thì sẽ được application tạo ra. Mỗi khi user mở folder đấy lên sẽ nhìn thấy 3 file image1.jpg, image2.jpg, image3.jpg. Nếu user bình thường thì mở 3 file đều trả về dữ liệu đã mã hóa. Nếu user là “phula” thì mở ra sẽ nhìn được nội dung file ảnh 1 cách bình thường.
  Gợi ý: Ở đâu đó trong máy tính sẽ lưu trữ 3 file ảnh ở dạng mã hóa, nếu user bình thường thì ở hàm đọc file sẽ đọc từ file ảnh mã hóa rồi trả về cho read buffer, nếu user là phula thì sẽ tiến hành giải mã rồi mới trả về cho read buffer.

## Slide 20: Thank you